## Slide 1: DAFP 3D Die Map
3D Die Map Definition
  128, 256 or 512 profiles are taken in the X direction, equally spaced from each other in the Y direction
  Nanoscope then assembles the individual profiles into an AFM like image, the 3D Die Map
  Once the die map has been assembled the image may be analyzed using the standard AFM analyses
  The example at right is a 25 mm x 25 mm 3D Die map from the SEMATECH MIT Mask CMP wafer showing Dishing and Erosion of Cu lines in ILD.